## Slide 1: Autodesk AEC Developer’s Camp 2010 Creating & Analyzing Massing Geometry With Revit API
Harry Mattison
Principal Engineer – Revit API Development
Notes: AEC Title

## Slide 2: Conceptual Massing in Revit
Ability to develop complex shapes
Extensive API access to geometry creation, manipulation, and analysis
Use Massing API with geometry, family, and .NET API for wide range of applications
  Geometry Creation
  Design Aids
  Analysis Tools

## Slide 3: Reference Points
Construction element for defining a curve’s path
Can be placed using XYZ coordinates
  Code example – Points on parabolic curves using NewReferencePoint(xyz) and math functions

## Slide 4: Reference Points with Geometric Constraints
Subclasses of PointElementReference
Constrain points to
  Edges
  Planes
  Faces
  Edge/edge intersections
  Edge/face intersections
  Code example – PointOnEdge-based points maintain relative location on edge as it changes

## Slide 5: Points from Different Data Sources
From Microsoft Excel From text file

## Slide 6: Curve By Points
Collect ReferencePoints into a ReferencePointArray for use by the NewCurveByPoints method.
Code Example:
Sine Curve

## Slide 7: Forms - 2D & 3D shapes from curves
Loft NewLoftForm(bool isSolid,ReferenceArray profiles)
Swept Blend NewSweptBlendForm(bool isSolid, ReferenceArray path, ReferenceArray profiles)
Revolve NewRevolveForm(bool isSolid, ReferenceArray profile, Reference axis, double startAngle, double endAngle)

## Slide 8: More Form Types
Extrusion NewExtrusionForm(bool isSolid, ReferenceArray profile, XYZ direction)
Cap Surface NewFormByCap(bool isSolid, ReferenceArray profile)
Thickened Surface NewFormByThickenSingleSurface(bool isSolid, Form singleSurfaceForm, XYZ thickenDir)

## Slide 9: Divided Surface
Creates a grid of parallelograms defined by:
  Grid rotation
  Spacing in the U & V directions
  and other parameters
  NewDividedSurface code example:

## Slide 10: Panel Creation API Tools

## Slide 11: Tile Patterns
Applied to Divided Surfaces
Defines type of panel family that the surface will use
Tile Pattern iteration code sample

## Slide 12: Driving Parameters from Different Data Sources
From Revit Geometry

## Slide 13: Driving Parameters from Different Data Sources
From Image File

## Slide 14: Driving Parameters from Different Data Sources
From random numbers

## Slide 15: Build Masses From RVT Geometry
Mass Surfaces from Room Boundaries
In the RVT
  Get all rooms
  Get 3D volume with room.ClosedShell
  Create mesh with face.Triangulate()
  Find vertices of each triangle in mesh
In the massing family
  Create point for each mesh vertex
  Create CurveByPoints between these points
  Create surfaces through these CurveByPoints using NewFormByCap
  Create subcategory and color for the surfaces related to each room.
Mass Surfaces & Levels from RVT to RFA (Context Creator)